## Slide 1
18PYB101J Module-I Lecture-9
ENERGY BAND STRUCTURE OF SEMICONDUCTOR & CONCEPTS OF EFFECTIVE MASS
18PYB103J Module-I Lecture-1
DEPARTMENT OF PHYSICS
SRM INSTITUTE OF SCIENCE AND TECHNOLOGY
18PY103J – Physics: Semiconductor Physics
Module-I, Lecture-9

## Slide 2
Energy Band Structure of Semiconductor
Brillouin zone
18PYB101J Module-I Lecture-9
To understand the Energy band structure, consider silicon atom. A schematic representation of an isolated silicon atom is shown in Figure.
Ten of the 14 silicon atom electrons occupy deep-lying energy levels close to the nucleus. The four remaining valence electrons are relatively weakly bound and are the electrons involved in chemical reactions.

## Slide 3
18PYB101J Module-I Lecture-9
Above Figure shows the band splitting of silicon. We need only to consider the n=3 level for the valence electrons, since the first two energy shells are completely full and are tightly bound to the nucleus.
The 3s state corresponds to n=3 and l=0 and contains two quantum states per atom. This state will contain two electrons at T= 0 K. The 3p state corresponds to n= 3 and l=1 and contains six quantum states per atom. This state will contain the remaining two electrons in the individual silicon atom.
Energy Band Structure of Semiconductor
Brillouin zone

## Slide 4
18PYB101J Module-I Lecture-9
As the interatomic distance decreases, the 3s and 3p states interact and overlap (covalent bonding and crystal formation).
At the equilibrium interatomic distance, the bands have again split, but now four quantum states per atom are in the lower band and four quantum states per atom are in the upper band.
At absolute zero degrees, electrons are in the lowest energy state, so that all states in the lower band (the valence band) will be full and all states in the upper band (the conduction band) will be empty.
The bandgap energy Eg between the top of the valence band and the bottom of the conduction band is the width of the forbidden energy band.
Energy Band Structure of Semiconductor
Brillouin zone

## Slide 5
18PYB101J Module-I Lecture-9
At T = 0 K, the 4 N states in the lower band, the valence band, are filled with the valence electrons. All of the valence electrons are in the valence band. The upper energy band, the conduction band, is completely
empty at T = 0 K.
As the temperature increases above 0 K, a few valence band electrons may gain enough thermal energy to break the covalent bond and jump into the conduction band.
This means that, as the negatively charged electron breaks away from its covalent bonding position, a positively charged “empty state” is created in the original covalent bonding position in the valence band.
As the temperature further increases, more covalent bonds are broken, more electrons jump to the conduction band, and more positive “empty states” are created in the valence band.
Energy Band Structure of Semiconductor
Brillouin zone

## Slide 6
18PYB101J Module-I Lecture-9
This bond breaking can be related to the E versus k energy bands(first brillouin zone).
Figure shows the E versus k diagram of the conduction and valence bands at T=0 K. The energy states in the valence band are completely full and the states in the conduction band are empty.
Energy Band Structure of Semiconductor
Brillouin zone

## Slide 7
18PYB101J Module-I Lecture-9
Below Figure shows these same bands for T >0 K, in which some electrons have gained enough energy to jump to the conduction band and have left empty states in the valence band.
Energy Band Structure of Semiconductor
Brillouin zone

## Slide 8
18PYB101J Module-I Lecture-9
The movement of an electron in a lattice will, in general, be different from that of an electron in free space.
In addition to an externally applied force, there are internal forces in the crystal due to positively charged ions or protons and negatively charged electrons, which will influence the motion of electrons in the lattice.
Then
Ftotal = Fext + Fint = ma (1)
where Ftotal, Fext, and Fint are the total force, the externally applied force, and the internal forces, respectively, acting on a particle in a crystal. The parameter a is the acceleration and m is the rest mass of the particle.
Electron Effective Mass

## Slide 9
18PYB101J Module-I Lecture-9
Since it is difficult to take into account all of the internal forces, the equation becomes
Fext = m*a (2)
where the acceleration a is now directly related to the external force. The parameter m*, called the effective mass, takes into account the particle mass and also takes into account the effect of the internal forces.
To use an analogy for the effective mass concept, consider the difference in motion between a glass marble in a container filled with water and in a container filled with oil. In general, the marble will drop through the water at a faster rate than through the oil. The external force in this example is the gravitational force and the internal forces are related to the viscosity of the liquids. Because of the difference in motion of the marble in these two cases, the mass of the marble would appear to be different in water than in oil.
Electron Effective Mass

## Slide 10
18PYB101J Module-I Lecture-9
The effective mass of an electron in a crystal can be related to the E versus k curves. E-k curves of semiconductor material contains allowed energy bands that are almost empty of electrons and other energy bands that are almost full of electrons.
Recalling Equation, the energy and momentum are related by
E = p2/2m = ħ2k/2m (3)
where m is the mass of the electron. The momentum p and wave number k are related by p=ħk . Taking the derivative of Equation (3) with respect to k,
dE/dk = ħ2k/m = ħp/m (4)
Relating momentum to velocity, Equation (4) can be written as
(1/ħ)(dE/dk )= p/m = v (5)
where v is the velocity of the particle. The first derivative of E with respect to k is related to the velocity of the particle.
Electron Effective Mass

## Slide 11
18PYB101J Module-I Lecture-9
If we now take the second derivative of E with respect to k, we have
d2E/dk2 = ħ2/m (6)
Equation (6) can be rewritten as
(1/ħ2)d2E/dk2 = 1/m* (7)
The second derivative of E with respect to k is inversely proportional to the mass of the particle. For the case of a free electron, the mass is a constant (non relativistic effect), so the second derivative function is a constant.
If we apply an electric fi eld to the free electron and use Newton’s classical equation of motion, then
Fext = m* a = eE (8)
where a is the acceleration, E is the applied electric field, and e is the magnitude of the electronic charge.
Electron Effective Mass

## Slide 12
18PYB101J Module-I Lecture-9
The effective mass is a parameter that relates the quantum mechanical results to the classical force equations.
In most instances, the electron in the bottom of the conduction band can be thought of as a classical particle whose motion can be modeled by Newtonian mechanics, provided that the internal forces and quantum mechanical properties are taken into account through the effective mass.
If we apply an electric field to the electron in the bottom of the allowed energy band, then the acceleration is
a = eE/m* (9)
where m* is the effective mass of the electron.
Electron Effective Mass