## Slide 1
Solar Cell
18PYB103J Module-III Lecture-14
DEPARTMENT OF PHYSICS
SRM INSTITUTE OF SCIENCE AND TECHNOLOGY
18PYB103J – Physics: Semiconductor Physics
Module-III, Lecture-14

## Slide 2
A solar cell is a pn junction device with no voltage directly applied across the junction. The solar cell converts photon power into electrical power and delivers this power to a load.
The pn Junction Solar Cell
Consider the pn junction shown in Fig. 1, with a resistive load. Even with zero bias applied to the junction, an electric field exists in the space charge region as shown in the Fig. 1.
Solar Cell
18PYB103J Module-III Lecture-14
Figure 1 | A pn junction solar cell with resistive load.

## Slide 3
Incident photon illumination can create electron-hole pairs in the space charge region that will be swept out producing the photocurrent IL in the reverse-biased direction as shown in Fig. 1.
The photocurrent IL produces a voltage drop across the resistive load which forward biases the pn junction. The forward-bias voltage produces a forward-bias current IF as indicated in the Fig. 1.
The net pn junction current, in the reverse-biased direction, is
here the ideal diode equation has been used.
18PYB103J Module-III Lecture-14
Solar Cell

## Slide 4
As the diode becomes forward biased, the magnitude of the electric field in the space charge region decreases, but does not go to zero or change direction. The photocurrent is always in the reverse-biased direction and the net solar cell current is also always in the reverse-biased direction.
There are two limiting cases of interest.
First limiting case is the short-circuit condition occurs when R = 0 so that V = 0. The current in this case is referred to as the short-circuit current,
Or
18PYB103J Module-III Lecture-14
Solar Cell

## Slide 5
The second limiting case is the open-circuit condition and occurs when R →∞.
The net current is zero and the voltage produced is the open-circuit voltage Voc. The photocurrent is just balanced by the forward-biased junction current, so we have
Then can find the open circuit voltage Voc as
where Vt = nkT/q
18PYB103J Module-III Lecture-14
Solar Cell

## Slide 6
18PYB103J Module-III Lecture-14
Solar Cell
A plot of the diode current I as a function of the diode voltage V from Eqn (4) is shown in Fig. 2. We may note the short-circuit current and open circuit voltage points on the figure.
The power delivered to the load is
Figure 2 | I–V characteristics of a pn junction solar cell.

## Slide 7
18PYB103J Module-III Lecture-14
Solar Cell
We may find the current and voltage which will deliver the maximum power to the load by setting the derivative equal to zero, or dP/dV = 0.
Using Eqn. (5), we find
where Vm is the voltage that produces the maximum power.
We may rewrite Eqn. (6) in the form

## Slide 8
18PYB103J Module-III Lecture-14
Solar Cell
The value of Vm may be determined by trial and error. Figure 3 shows the maximum power rectangle where Im is the current when V = Vm.
Figure 3 | Maximum power rectangle of the solar cell I–V characteristics.

## Slide 9
18PYB103J Module-III Lecture-14
Solar Cell
Efficiency of a Solar Cell:
To determine the efficiency of the solar cell following parameters are to be described
Short-Circuit Current Isc
The short-circuit current is the current through the solar cell when the voltage across the solar cell is zero (i.e., when the solar cell is short circuited).
Here Short-Circuit Current is nothing but light generated current.

## Slide 10
18PYB103J Module-III Lecture-14
Solar Cell
Open-Circuit Voltage VOC
The open-circuit voltage, VOC, is the maximum voltage available from a solar cell, and this occurs at zero current. The open-circuit voltage corresponds to the amount of forward bias on the solar cell due to the bias of the solar cell junction with the light-generated current.
Fill Factor FF
Fill Factor FF, is a measure of the realizable power from a solar cell. Typically, the fill factor is between 0.7 and 0.8. The FF is defined as the ratio of the maximum power from the solar cell to the product of Voc and Isc so that

## Slide 11
18PYB103J Module-III Lecture-14
Solar Cell
Conversion Efficiency 
The conversion efficiency  of a solar cell is defined as the ratio of output electrical power to incident optical power. For the maximum power output, we can write
The maximum possible current density and the maximum possible voltage in the solar cell are Isc and Voc, respectively.

## Slide 12
18PYB103J Module-III Lecture-14
Solar Cell
The conventional pn junction solar cell has a single semiconductor bandgap energy. When the cell is exposed to the solar spectrum, a photon with energy less than Eg will have no effect on the electrical output power of the solar cell.
A photon with energy greater than Eg will contribute to the solar cell output power, but the fraction of photon energy that is greater than Eg will eventually only be dissipated as heat.
The maximum efficiency of a silicon pn junction solar cell is approximately 28 percent. Non ideal factors, such as series resistance and reflection from the semiconductor surface, will lower the conversion efficiency typically to the range of 10 to 15 percent.

## Slide 13
18PYB103J Module-III Lecture-14
Solar Cell
Figure 4 | Ideal solar cell efficiency at T = 300 K for C = 1 sun and for a C =1000 sun concentrations as a function of bandgap energy.

## Slide 14
18PYB103J Module-III Lecture-14
Solar Cell
A large optical lens can be used to concentrate sunlight onto a solar cell so that the light intensity can be increased up to several hundred times. The short-circuit current increases linearly with light concentration while the open-circuit voltage increases only slightly with concentration.
We can see that the conversion efficiency increases only slightly with optical concentration through Fig. 4. The primary advantage of using concentration techniques is to reduce the overall system cost since an optical lens is less expensive than an equivalent area of solar cells.

## Slide 15
18PYB103J Module-III Lecture-14
Solar Cell
Loss in Solar Cell : Factors which affect Efficiency of the Solar Cell
Loss due to Low Energy Photons (h < Eg)
Loss due to High Energy Photons (h > Eg)
Voltage Loss
Fill Factor Loss
Loss due to Reflection
Loss due to less Absorption
Loss due to covering of Metal Contact
Recombination Loss